## Slide 1: Electricity Distribution Network & Green Transition
Elektro Ljubljana OVE Ltd.

## Slide 2: Electricity consumption growth expectations
National Energy and Climate Plan (NECP = NEPN) estimates 70% increase in electric power generation till 2050.
Todays primary energy supply of Slovenia is at the level of 70 TWh.
If we don‘t implement totally new technologies not known yet, increase in electricity demand will be much higher.
To become CO2 neutral society, estimation of needed green electricity generation goes up to almost 40 TWh (double the values from NECP)
Source: NEPN, MZI 2020

## Slide 3
By 2050 in SLO 40 GW mostly distributed generation capacity is expected while today‘s total electric energy generation capacity is about 3 GW.
RES mostly connected to the distribution network, where today only about 0,4 GW is connected.
Distribution of 40 TWh of energy instead of today‘s 12,5 TWh.
In ideal case minimum needed increase in network capacity is 250-300%, but probably close to 400%.
With today‘s investment, we increase network capacity by 1,5 – 3 % / year -> could take up to 100 years.
Increase of investment for at least 300% is needed.
CO2 neutrality
Impact on Electric Energy Distribution Network

## Slide 4: EU estimates
Power Barometer (Eurelectric) estimates the investment needs into the distribution network to double from 33,5 billion EUR/year to 60 during 2021-2030.
EU commission estimates these needs to 60 to 110 billion EUR/year (200 - almost 400%).
Our estimates are at 350%.
Imagine influence on network tariffs and costs for EE and consequentially competitiveness of EU economy.
Where to find founds and human resources?
Distribution network needs all possible support to follow these trends and overcome all bottlenecks on that way.
Source: Power Barometer, Eurelectric, 2019.
EU commission estimate need to increase investments in electric power networks in Slovenia from 150 to 170 M EUR (DSO and TSO) to 240 to 450 M EUR each year.

## Slide 5
Most strategies of sustainable development relays on electrification of heating.
At EU level, already by 2030 four (4) times more heat pumps is estimated, then now.
In SLO number of heat pumps rises very quickly.
Their total electric capacity is already over 270 MW (13% of peak load of the country).
Estimated number of heat pumps for 2030 is 200.000 with total loading of additional 950 MW.
In 2019 number of heat pumps increased for 53 %. Istalled capacity rised for 67 MW.
Source: Eco fund. Picture: Elektro Maribor, 2020.
Causes of demand increase
Electric heating with Heat Pumps

## Slide 6
National goal of transport electrification is set to 200.000 EVs in 2030:
  200.000 EVs will increase peak loading of the distribution network for 400 MW, if done in today‘s manner
  20% of todays peak power.
1.000.000 cars by 2050 -> ?? MW
Transport of goods, air transport, sea/water ways transport -> MW
Source: The impact of mass electrification of passenger traffic and heating on the development of the distribution network , EIMV, 2018.
In 2020 less than 1000 electric cars (BV) were sold in Slovenia.
To reach 2030 target, 20.000 should be sold every year.
Causes of demand increase
E – mobility

## Slide 7
Experiences show, that RES do not decrease network loading, but increase it.
PV generation does not correspond to the power needs in time.
In 2020, 370 MW PV sources installed generated 0,29 TWh – we are on 0,75% way to carbon neutrality.
To reach 2030 RES targets, we need to increase construction intensity by 10x.
Source: Elektro Ljubljana (2016 – 2020)
Causes of demand increase
RES integration

## Slide 8
  Simplify building permit procedures and decrease associated costs (network improvement is precondition for carbon neutral society and supposed to be in public interest! – is it?)
  Adapt regulation to be stimulative for the network owners to improve the system
  Coordinate spatial planning with actual state of distribution network and most effective possibilities for development
  Make also Renewable Energy Source operators to take share in responsibility for power quality parameters in the network
Source: Slovenian DSO-s 2019. Picture: Elektro Maribor, 2020.
How to support faster Electric Energy Distribution Network development
Source: Slovenian DSO-s 2019. Picture: Elektro Maribor, 2020.

## Slide 9: Problems in getting construction permits SLO example -NATURA 2000
There are 355 protected areas in the frame NATURA 2000 in Slovenia
These areas are covering 37,46 % of the surface of entire country of Slovenia
Due to complicated procedures, considerable parts of project costs are spent only to get permission to build.
Procedures take up to 10 years
Source: http://www.natura2000.si

## Slide 10: How DSO can contribute
Energy efficiency reduces emissions.
Losses reduction (I2R) is best contribution, distribution can give.
Very small potential limited with power quality.
RES have generally opposite effect.
Source: CEER report on power losses 2020

## Slide 11: Power Quality parameters
Not only the shape and amplitude of voltage sinusoidal
Also interruptions in the power supply
Different influences on the grid!
Need of higher cap
Source: CEER benchmark report 2018

## Slide 12: Network construction
The most efficient way to robust network? Underground cables!
No smart solution is more effective!
DSO-s need support to bring the network underground and essentially increase capacity.
Souce: CEER benchmark report 2018

## Slide 13: Whom to contact?
For more information, please contact
Damjan Kresal
Elektro Ljubljana OVE Ltd.
damjan.kresal@el-ove.si